Tips on using an Ultima Combo TENS/EMS device

The following guidelines are tips on using the TENS/EMS Combo device.  Please consult your physician for complete instructions. Please note: the chosen settings on a TENS/EMS device will vary depending on your comprehensive treatment program as defined by the treating physician.

TENS/EMS Set-up:

- Place the battery in the device, and turn on by pressing the power button   (this is just for set-up turn device off before attaching the lead wires.

- Choose the appropriate TENS or EMS treatment setting as prescribed by your physician. TENS preset modes are P0-P11 while TENS manual modes are P12-P19 and are selected by pressing the (Prog) button.  To switch from TENS to EMS settings hold the (Prog) button for 6 seconds. EMS preset modes are P20-P29 while EMS manual modes are P30-P33. Refer to page 12 in the user's manual for a full explanation of each button.

- Wash the skin area gently with water and dry thoroughly (placement site).

- Be sure the device is turned off before connecting the lead wires to the electrodes.

- Connect the lead wires into the electrodes.  Try to use both channels (4 pads) for polarity reasons.

- Place the electrodes—at least 2 inches apart—but not further than 4 inches.

- Plug in the lead wires to the electrode pads.

- Set the intensity knobs (up top) to a level that is strong (intense), but comfortable (0-20).

- Carry the TENS/EMS device by using the belt clip and be sure to turn down the intensity if you need to move around.

After using the TENS/EMS unit

- Before turning off the EMS device, record the location of the electrodes, the settings of all controls, and your progress in reducing pain.

- Turn both intensity controls to 0. Unplug the lead wires, grasping the plug, not the cord.

- Remove the electrodes by carefully peeling them off. Clean the skin and the electrodes thoroughly with water, dry and place back in air-tight package.

- If the TENS/EMS device has a rechargeable battery system, then it is recommended that the unit be recharged when not in use.

Do . . .

- Remove the electrodes and discontinue stimulation if you experience skin irritation.

- Contact your clinician with any questions.

- Keep the TENS/EMS device clean.

- Clean the lead wires with only water and mild soap.

- Turn both intensity knobs to 0 before replacing the battery.

- Use only manufacturer’s recommended electrodes, tape, patches, lead wires, and electrode gels.

Don’t . . .

- Use rubbing alcohol to decrease excessive oiliness of the skin, use a clean-cote™ wipe.

- Use rubbing alcohol, Freon, or any other solvent on the lead wires as these materials will cause the lead wires to lose their flexibility and significantly reduce their effectiveness.

- Drop, bump, or use the unit roughly.

- Engage in contact sports when using EMS.

- Get the device wet. (A damp cloth can be used to clean the exterior of the unit.)

- Pull or kink the lead wires.

- Use the unit while operating a motor vehicle.

- Use the device while operating machinery such as power tools.

- Allow electrodes to touch each other during stimulation or improper stimulation. This will shorten the life of the battery.